## Slide 1
ENTERPRISE NETWORK SECURITY BRIEFING
IPsec VPN
Secure Communication Over Untrusted Networks
From Protocol Theory to Live Cisco Implementation
ENCRYPTED TUNNEL
Cyber Security · Networking · Cisco IOS
Team 3 · Mohammed Hany Mamdouh · Ahmed Ehab Mohamed · Ahmed Samir Ibrahim

## Slide 2
AGENDA
What We'll Cover
PART ONE
Foundations & Protocol Theory
1
What is a VPN & why IPsec
2
IPsec core protocols — AH, ESP, IKE, SA
3
Transport vs Tunnel mode
4
IKE phases & versions
5
How a secure tunnel is established
6
Site-to-Site vs Remote Access VPN
7
Algorithms, NAT traversal & best practice
8
Advantages & limitations
PART TWO
Live Implementation — Cisco Lab
1
Topology & network setup (R1 · R2 · R3)
2
Phase 1 — IKE / ISAKMP configuration
3
Phase 2 — IPsec data tunnel configuration
4
Full running configuration walkthrough
5
Verification & active Security Associations
6
Key insights from the lab
7
Conclusion & takeaways
IPSEC VPN | SECURE COMMUNICATIONS
02 / 24

## Slide 3
FOUNDATIONS
What Is a VPN?
A Virtual Private Network (VPN) extends a private network across a public, untrusted network — typically the Internet — creating a logical, encrypted tunnel between two points.
Confidentiality
Keep sensitive data private while it crosses a public network.
Remote Access
Let employees reach internal resources securely from anywhere.
Site Interconnection
Join branch offices or data centers as one logical network.
User
Internet
Private Network
ENCRYPTED TUNNEL
Internal resources reachable as if directly connected
IPSEC VPN | SECURE COMMUNICATIONS
03 / 24

## Slide 4
FOUNDATIONS
What Is IPsec?
IPsec (IP Security) is a framework of open standards, developed by the IETF, that provides security for IP traffic. It operates at the network layer (Layer 3), protecting and authenticating IP packets between peers — without requiring changes to applications above it.
Confidentiality
Encryption hides data from unauthorized viewers.
Data Integrity
Detects if data was altered in transit.
Origin Authentication
Confirms the identity of the sending peer.
Anti-Replay
Rejects old or duplicated captured packets.
Defined across RFC 4301 (Security Architecture) and companion RFCs consolidated in RFC 6071.
IPSEC VPN | SECURE COMMUNICATIONS
04 / 24

## Slide 5
ARCHITECTURE
IPsec Core Building Blocks
AH
Authentication Header
Provides data integrity and origin authentication for the IP packet. No encryption. Defined in RFC 4302; optional in the current IPsec architecture.
ESP
Encapsulating Security Payload
Provides confidentiality (encryption) plus optional integrity and authentication. Defined in RFC 4303; used in virtually all deployments.
IKE
Internet Key Exchange
Automates peer authentication and negotiates the keys and algorithms (SAs) that AH/ESP will use, so keys don't need manual configuration.
SA
Security Association
A unidirectional agreement between two peers on the protocol, algorithms, and keys used to protect a specific data flow.
IPSEC VPN | SECURE COMMUNICATIONS
05 / 24

## Slide 6
ARCHITECTURE
AH vs ESP
AH
ESP
Confidentiality (encryption)
No
Yes
Data integrity
Yes
Yes
Origin authentication
Yes
Yes
Anti-replay protection
Yes (optional)
Yes (optional)
Encapsulates the payload
No
Yes
Defining RFC
RFC 4302
RFC 4303
Status today
Optional
Mandatory (MUST)
Defining RFC
RFC 4302
RFC 4303
IPSEC VPN | SECURE COMMUNICATIONS
06 / 24

## Slide 7
ARCHITECTURE
Transport Mode vs Tunnel Mode
TRANSPORT MODE
Only the payload of the IP packet is protected. The original IP header stays in place. Typically used for direct, end-to-end host-to-host communication.
IP Header
Encrypted Payload (ESP)
Used for: host-to-host IPsec sessions
TUNNEL MODE
The entire original IP packet is encrypted and encapsulated inside a new IP packet with a new header. Standard mode for gateway-to-gateway (site-to-site) VPNs.
New IP Header
Encrypted Original Packet (IP Header + Payload)
Used for: site-to-site & remote-access VPNs
IPSEC VPN | SECURE COMMUNICATIONS
07 / 24

## Slide 8
KEY MANAGEMENT
IKE: Phases & Versions
IKEv1 — RFC 2409
Phase 1
Authenticates the peers and builds a secure ISAKMP SA (Main Mode — protects identities, or faster Aggressive Mode).
Phase 2
Quick Mode uses the Phase 1 channel to negotiate the actual IPsec (AH/ESP) SAs and keying material.
IKEv2 — RFC 7296
Combines ISAKMP, key exchange and negotiation into one streamlined protocol (originally RFC 4306, consolidated into RFC 7296). Not interoperable with IKEv1.
Fewer round trips — faster setup
Built-in NAT traversal & Dead Peer Detection
Native support for EAP / remote-access auth
Mobility support via MOBIKE
IPSEC VPN | SECURE COMMUNICATIONS
08 / 24

## Slide 9
PROCESS
How a Secure Tunnel Is Established
1
Interesting Traffic
Traffic matches a configured crypto policy (ACL) and triggers IPsec.
2
IKE Phase 1
Peers authenticate each other and build a secure control channel.
3
IKE Phase 2
Peers negotiate the IPsec SA — algorithms and keying material.
4
Secure Tunnel
AH/ESP now protect data using the agreed keys and algorithms.
5
SA Teardown
SAs expire or are cleared; new keys are negotiated as needed.
IPSEC VPN | SECURE COMMUNICATIONS
09 / 24

## Slide 10
DEPLOYMENT
Site-to-Site vs Remote Access
SITE-TO-SITE VPN
Connects two networks permanently through their firewalls/routers (gateways). Always uses tunnel mode. Ideal for linking branch offices or data centers.
Office A
Gateway
Office B
Static peers · Always-on · Transparent to users
REMOTE ACCESS VPN
Connects an individual client with a dynamic IP to a corporate gateway. IKE mode configuration assigns the client an internal address as part of negotiation.
Remote User
Gateway
Dynamic peers · On-demand · Per-user authentication
IPSEC VPN | SECURE COMMUNICATIONS
10 / 24

## Slide 11
CRYPTOGRAPHY
Algorithms & Current Best Practice
Encryption
AES-CBC / AES-GCM
128-bit minimum, 256-bit for high assurance
3DES, DES
No longer recommended
Integrity
HMAC-SHA-256 / 384 / 512
Recommended replacement for SHA-1
HMAC-MD5
Avoid for new deployments
Key Exchange (DH)
Group 14+ (2048-bit) / ECDH
Recommended minimum since 2013
Groups 1, 2, 5 (≤ 1536-bit)
Too weak
Guidance reflects Cisco IOS XE hardening (17.11.1a+) and IETF cryptographic algorithm requirement RFCs.
IPSEC VPN | SECURE COMMUNICATIONS
11 / 24

## Slide 12
PRACTICAL CONSIDERATIONS
NAT Traversal & Firewall Rules
The Problem
Network Address Translation (NAT) rewrites IP/port information in packet headers. This breaks AH's integrity check and complicates ESP, since NAT devices historically expect TCP/UDP ports that ESP alone does not provide.
The Fix: NAT-T
NAT-Traversal (RFC 3947 for IKE negotiation, RFC 3948 for encapsulation) detects NAT devices between peers and wraps ESP packets inside UDP so they can pass through the NAT unmodified.
REQUIRED FIREWALL RULES
Allow UDP port 500 (IKE)
Allow UDP port 4500 when NAT-T is used
Allow ESP — IP protocol 50
Allow AH — IP protocol 51
Recommendation: use static NAT and apply it before IPsec encapsulation whenever possible.
IPSEC VPN | SECURE COMMUNICATIONS
12 / 24

## Slide 13
EVALUATION
Advantages & Limitations
Advantages
Strong, standards-based security services
Transparent to applications — no app changes needed
Widely supported across vendors & platforms
Protects any IP traffic, not just a single app
Limitations
Configuration complexity, especially at scale
NAT compatibility requires extra handling
Encryption/decryption adds processing overhead
Designed for unicast; multicast needs extensions
IPSEC VPN | SECURE COMMUNICATIONS
13 / 24

## Slide 14
PART TWO
From Theory to Practice
Live Site-to-Site IPsec VPN Implementation on Cisco IOS
Topology
IKE Phase 1
IPsec Phase 2
Verification
IPSEC VPN | SECURE COMMUNICATIONS
14 / 24

## Slide 15
LIVE IMPLEMENTATION
Lab Topology & Network Setup
PC-A
PC-C
IPsec TUNNEL
R1 — Branch A
192.168.1.0/24
R2 — WAN / ISP
Pass-through only
R3 — Branch B
192.168.3.0/24
R1 (Branch A)
Local LAN 192.168.1.0/24 hosting PC-A.
R2 (WAN ISP)
Intermediary router connecting R1 and R3 without VPN awareness.
R3 (Branch B)
Local LAN 192.168.3.0/24 hosting PC-C.
Routing Base
OSPF Area 0 enabled across all routers for underlying reachability.
IPSEC VPN | SECURE COMMUNICATIONS
15 / 24

## Slide 16
LIVE IMPLEMENTATION
Live Lab Evidence — Topology & Connectivity
REAL LAB EVIDENCE
Captured directly from the Cisco Packet Tracer implementation before the IPsec tunnel is configured.
PACKET TRACER — LOGICAL TOPOLOGY & PDU TEST RESULTS
WHY THIS EVIDENCE MATTERS
Real lab, real topology
PC-A – R1 – R2 (pass-through) – R3 – PC-C matches the addressing table exactly.
OSPF underlay confirmed
ICMP tests to Router1, Router2, and PC1 all return Successful — routing works end to end.
Clean baseline before IPsec
No crypto map is active yet, so this connectivity is plain, unencrypted routing.
Sets up the tunnel evidence
Any encryption seen on the next slides is provably caused by IPsec, not by chance.
IPSEC VPN | SECURE COMMUNICATIONS
16 / 24

## Slide 17
LIVE IMPLEMENTATION
Phase 1: IKE / ISAKMP Configuration
ISAKMP Policy 10
Defines control-plane security parameters.
Encryption: AES-256
Hash: SHA
Lifetime: 3600s (1 hour)
Authentication
Uses Pre-Shared Keys (PSK) for peer validation.
Key string: cisco123
R1 → peer R3 (10.2.2.1)
R3 → peer R1 (10.1.1.1)
Key Exchange
Establishes a shared, secure management channel.
Diffie-Hellman Group 5
Encrypted ISAKMP channel
Prepares for Phase 2
IPSEC VPN | SECURE COMMUNICATIONS
17 / 24

## Slide 18
LIVE IMPLEMENTATION
Phase 2: IPsec Data Tunnel Configuration
1
Transform Set
Specifies payload encryption & integrity algorithms.
crypto ipsec transform-set 50
esp-aes 256 esp-sha-hmac
2
Interesting Traffic
ACL defines the traffic that triggers encryption.
access-list 101 permit ip
192.168.1.0/24 192.168.3.0/24
3
Crypto Map
Binds peer IP, ACL, and transform set together.
crypto map CMAP 10 ipsec-isakmp
(applied to WAN interface)
IPSEC VPN | SECURE COMMUNICATIONS
18 / 24

## Slide 19
LIVE IMPLEMENTATION
Full Running Configuration — R1 (Cisco IOS)
A complete site-to-site tunnel using IKEv1 with AES-256 and SHA, in tunnel mode — matching the lab topology on the previous slides.
R1-BranchA# show running-config
crypto isakmp policy 10
encryption aes 256
authentication pre-share
group 24
crypto isakmp key cisco123 address 10.2.2.1
!
crypto ipsec transform-set 50 esp-aes 256 esp-sha-hmac
!
access-list 101 permit ip 192.168.1.0 0.0.0.255 192.168.3.0 0.0.0.255
!
crypto map CMAP 10 ipsec-isakmp
set peer 10.2.2.1
set transform-set 50
match address 101
!
interface GigabitEthernet0/0/0
crypto map CMAP
IPSEC VPN | SECURE COMMUNICATIONS
19 / 24

## Slide 20
LIVE IMPLEMENTATION
Verification & Active Security Associations
show crypto isakmp sa
QM_IDLE
show crypto ipsec sa
5 / 5 encrypted
show crypto map
Peer 10.2.2.1 · ACL 101
IPSEC VPN | SECURE COMMUNICATIONS
20 / 24

## Slide 21
LIVE IMPLEMENTATION
Key Insights From the Lab
Dynamic Tunnel Activation
SAs are created on-demand only when “interesting traffic” (LAN-to-LAN packets) matches the defined ACL.
Uninteresting Traffic Behavior
Direct router-to-router pings or OSPF Hello packets pass through standard, unencrypted IP routing.
Local LAN Segment Security
Traffic between local hosts (e.g. PC-A) and the local router interface remains plaintext; encryption occurs upon exiting the WAN interface.
IPSEC VPN | SECURE COMMUNICATIONS
21 / 24

## Slide 22
WRAP-UP
Conclusion
IPsec secures IP traffic at the network layer using AH/ESP for data protection and IKE for automated key management — as demonstrated end-to-end in this session's live Cisco lab.
1
Tunnel mode + ESP is the practical default for real-world site-to-site and remote-access VPNs.
2
IKEv2 (RFC 7296) is the modern, recommended standard — faster, more resilient, and NAT-friendly by design.
3
Strong outcomes depend on current algorithms: AES, SHA-2, and 2048-bit+ / elliptic-curve Diffie-Hellman.
4
The Cisco lab confirmed the theory in practice: ISAKMP + transform sets + crypto maps reliably brought up an encrypted, verifiable tunnel between two branch sites.
IPSEC VPN | SECURE COMMUNICATIONS
22 / 24

## Slide 23
SOURCES
References
S. Frankel & S. Krishnan, “IPsec/IKE Roadmap”, RFC 6071, IETF, Feb. 2011.
S. Kent & K. Seo, “Security Architecture for the Internet Protocol”, RFC 4301, IETF, Dec. 2005.
C. Kaufman et al., “Internet Key Exchange Protocol Version 2 (IKEv2)”, RFC 7296, IETF, Oct. 2014.
A. Huttunen et al., “UDP Encapsulation of IPsec ESP Packets”, RFC 3948, IETF, Jan. 2005.
Cisco Systems, “Configuring Security for VPNs with IPsec”, Cisco IOS Security Configuration Guide.
Cisco Systems, “Configuring Internet Key Exchange for IPsec VPNs”, Cisco IOS Security Configuration Guide.
Cisco Networking Academy, “Site-to-Site IPsec VPN Lab Guide”, CCNA Security Lab 19.5.6.
IPSEC VPN | SECURE COMMUNICATIONS
23 / 24

## Slide 24
Thank You
Questions & Discussion
TEAM 3
Mohammed Hany Mamdouh • Ahmed Ehab Mohamed • Ahmed Samir Ibrahim
IPSEC VPN | SECURE COMMUNICATIONS
24 / 24